## Slide 2
Yizhou Xu, Intel
Mengxin Liu, Alauda
CNI-agnostic network performance accelerator with eBPF

## Slide 3
Agenda
TCP/IP stack overhead
eBPF background knowledge
How to bypass Tcp/Ip with eBPF
Performance Analysis
Practice on KubeVirt acceleration

## Slide 4
TCP/IP stack overhead
In Kubernetes, each pod has its own network stack, packet from one pod to another traverse whole stack multiple times
In particular, service mesh amplify the overhead by sidecar mode
Tcp/ip overhead in Pod to Pod (same host)
Tcp/ip overhead in Service Mesh (same host)
Notes: TCP/IP (Transmission Control Protocol/Internet Protocol) is the foundational protocol suite of the Internet and plays a crucial role in modern networking.
All the application data goes via sidecar (Envoy*)
All the data passes TCP/IP stack 3 times
  Inbound
  Outbound
  Envoy to Envoy (same host)

## Slide 5
Why use eBPF
Work in Kernel
Non-intrusive
CNI agnostic
Safety and efficient

## Slide 6
eBPF background knowledge – Map&Prog
MAP
provide generic data structure for user space
and kernel space communication
    HASHMAP
    SOCKHASH
Program type
    SOCK_OPS
    SK_MSG
Notes: sock_ops
    Set callbacks for TCP state changing
    Help functions: BPF_MAP_UPDATE_ELEM, BPF_SOCK_HASH_UPDATE
SK_MSG
    Attach to a SOCKHASH map, capture the packets sent by a socket in SOCKHASH map and determine its destination socket
    Help functions: BPF_MSG_REDIRECT_HASH

## Slide 7
Combining MAP & Program for acceleration
sock_ops
    capture socket in given status, populate into map
sk_msg
    when there is data in socket, lookup peer socket
    transfer data to peer

## Slide 8
Pod to Pod acceleration(Kubernetes)

## Slide 9
Inbound Acceleraion(Service Mesh)

## Slide 10
Outbound Acceleration(Service Mesh)

## Slide 11
Envoy to Envoy Acceleration (same host)

## Slide 12
It’s opensource!
  REPO: https://github.com/intel/istio-tcpip-bypass

## Slide 13
Benchmark
  Deploy two test Pods in the same Node
  Use qperf to benchmark TCP latency/bandwidth with packet sizes from 1byte to 16KB
    qperf -t 60 100.64.0.3 -ub -oo msg_size:1:16K:*4 -vu tcp_lat tcp_bw
  Compare with the benchmark when the optimization is disabled
Chart: TCP Latency
| 1 | 4 | 16 | 64 | 256 | 1024 | 4096 | 16384
eBPF(us) | 20.2 | 20.2 | 19.6 | 18.8 | 19.2 | 18.3 | 18.5 | 20.2
Default(us) | 44.5 | 48.7 | 41.6 | 41.3 | 36 | 42.4 | 62.6 | 58.8
Chart: TCP Bandwidth Ratio
| 1 | 4 | 16 | 64 | 256 | 1024 | 4096 | 16384
eBPF/Default | 0.3185 | 0.32814 | 0.34173 | 0.48159 | 0.73284 | 1.6076 | 1.8354 | 1.3913

## Slide 14
Benchmark Analysis
  TCP latency will decrease by 40% ~ 60%
  Throughput will increase by 40% ~ 80% when the packet size is greater than 1024 bytes
  When the packet size is less than 512 bytes, the throughput decrease due to per packet processing overhead

## Slide 15
KubeVirt network performance
  Native Kubevirt Bridge networks have a much larger performance gap compared to Pods.
    Latency increased by 60%
    PPS decreased by 50%.
  Possible causes:
    The consumption brought by the virtualized Linux network stack itself
    Additional losses caused by the multiple layers of KubeVirt Bridge network.
  Kata has already utilized tc-mirror to bypass the bridge

## Slide 16
KubeVirt network acceleration
  Both tc-mirror and bpf_redirect are tried
    tc-mirror performed slightly better than bpf_redirect in all tests
    tc-mirror do not require high version kernel
    We didn’t find way to redirect from VM eth0 to veth0 directly
    Latency decrease 5% but throughput decrease about 20%
  Disable checksum
    No need checksum for internal packet processing
    Both rx/tx are disabled
TC-Mirror

## Slide 17
Benchmark
  Use qperf to benchmark UDP latency/bandwidth with packet sizes from 1byte to 16KB
    Latency 4%~30% decrease
    Throughput 20%~70% improvement
Chart: UDP Bandwidth Ratio
| 1 | 4 | 16 | 64 | 256 | 1024 | 4096 | 16384
tc-mirror/Default | 1.561 | 1.5569 | 1.5399 | 1.6038 | 1.5052 | 1.2229 | 1.7099 | 1.4211

## Slide 18
Future work
  Accelerate UDP inter-node traffic
  Fine-grained control the switch between eBPF datapath and kernel network datapath
  Accelerate Kubevirt VMs traffic within the same Node

## Slide 19
Notice and Disclaimer
Intel technologies may require enabled hardware, software or service activation.
No product or component can be absolutely secure.
Your costs and results may vary.
© Intel Corporation. Intel, the Intel logo, and other Intel marks are trademarks of Intel Corporation or its subsidiaries. Other names and brands may be claimed as the property of others.